## Slide 1: Title
7-Segment Display Controller
Using Lookup Table Logic

## Slide 2: Objective
• Design a 7-segment display controller using Verilog HDL
• Convert 4-bit binary input into 7-segment output
• Simulate using Icarus Verilog and GTKWave

## Slide 3: Tools Used
• Visual Studio Code
• Icarus Verilog
• GTKWave

## Slide 4: Introduction
A 7-segment display is an electronic display device used to display decimal numbers.
The project converts binary inputs into segment control outputs.

## Slide 5: Working Principle
• Input: 4-bit binary number
• Case statement acts as lookup table
• Output controls segments a–g
• Correct digit appears on display

## Slide 6: Truth Table
0 → 1111110
1 → 0110000
2 → 1101101
3 → 1111001
4 → 0110011
5 → 1011011
6 → 1011111
7 → 1110000
8 → 1111111
9 → 1111011

## Slide 7: Verilog Design
The design module uses a case statement to map binary inputs to 7-segment patterns.

## Slide 8: Testbench
The testbench automatically changes input values from 0 to 9 every 10 time units.

## Slide 9: Simulation
Simulation is performed using Icarus Verilog.
Waveforms are viewed using GTKWave.

## Slide 10: Applications
• Digital clocks
• Calculators
• Elevators
• Scoreboards
• Microwave displays

## Slide 11: Advantages
• Simple design
• Easy debugging
• Fast implementation
• No complex Boolean equations

## Slide 12: Conclusion
The 7-segment display controller was successfully designed and simulated using Verilog HDL.